## Slide 1
1
Input Data
user provided sets and parameters
2
Constraints
8x linear, 1x quadratic
4
Solving
Python + Gurobi
Fleet
capacity, consumption, charging power, price, cycle warranty
Orders
routing for trips, chaining for routes, driving windows, filtering
Depot
baseline load, grid connection, PV generation, charging stations
Markets
private spot energy, public charging, diesel, toll
C1: Trip Coverage
every f ∈ F served by exactly one pair (m, s)
C2: Activity Exclusivity
one event per vehicle and time step
C3: Routing & Trips
depot-anchored routes, trip chaining
C4: Crew Rules
shift length, driving time, mandatory brakes
C5: SoC Dynamics
SoC tracking, trip metering, start/end target
C6: Power & Conversion
physical battery flow, charging
C7: Charger Allocation
select strongest station, power & energy caps
C8: Grid Coupling
site import, peak cap, PV allocation, V2V netting
Degradation modeling
ξ = SoCm,t–1 / Ecapm , w(ξ) = 1 + 4κ(ξ – 0.5)²
(energy-throughput + SoC-dependent ageing weight)
Bilinear product
wm,t · E–m,t (product of two decision variables  quadratic class)
Branch-and-cut
MIP-gap target, multi-processing, presolve and cuts, time limits
Solution
vehicle and driver route assignments, power and SoC timeline, cost composition, used vehicles and chargers
3
Objective
minimise daily cost
min C = Cenergy + Ctoll + Cfuel + Cdeg + Ccrew + ΔCpeak – RV2G – SV2V + Ψpen energy purchase + road toll + diesel + battery ageing + drivers + demand-charge - V2G revenue - vehicle-to-vehicle saving + modelling penalties
former MILP formulation:
new MIQCP formulation: